## Slide 2: Irrigation efficiency and optimization The Optirrig model
Bruno Cheviron, Claire Serra-Wittling, Juan-David Dominguez-Bohorquez, Magalie Delmas, Bruno Molle

## Slide 3
Water savings from improvements of... Irrigation efficiency
As defined in the "cascade scheme" of Serra-Wittling & Molle 2017
[Invited report for the French Ministry of Agriculture]
Color code
Fraction due to Rain Water
Fraction due to Irrigation Water

## Slide 4
Water savings from improvements of... Irrigation efficiency
Color code
Fraction due to Rain Water
Fraction due to Irrigation Water
Rationale
Calculation of efficiencies and losses in 5 successive stages from irrigation water distribution to crop transpiration
Complete mixing of rain water (RW) and irrigation water (IW) in soil with time-variable volume fractions carried on through the "cascade scheme"
Challenge for metrology and modelling: quite tricky to code but physically sound and yields promising results
As defined in the "cascade scheme" of Serra-Wittling & Molle 2017
[Invited report for the French Ministry of Agriculture]

## Slide 5
Leaks from
equipments
Water savings from improvements of... Irrigation efficiency
Stage 1
E=Ed=Ai/Pi
Applied
Brought in

## Slide 6
Leaks from
equipments
Wind drift
Water savings from improvements of... Irrigation efficiency
E=Ed.Ea=Si/Pi
Stage 2
Reaches soil
Brought in

## Slide 7
Leaks from
equipments
Wind drift
Runoff or
drainage
Water savings from improvements of... Irrigation efficiency
E=Ed.Ea.Es=Rzi/Pi
Stage 3
Stored in root zone
Brought in

## Slide 8
Leaks from
equipments
Wind drift
Runoff or
drainage
Weeds or
excessive storage
Water savings from improvements of... Irrigation efficiency
E=Ed.Ea.Es.Ec=AETi/Pi
Stage 4
Evapotranspirated
Brought in

## Slide 9
Leaks from
equipments
Wind drift
Runoff or
drainage
Weeds or
excessive storage
Evaporation
Water savings from improvements of... Irrigation efficiency
E=Ed.Ea.Es.Ec.Et=Tpi/Pi
Stage 5
Finally transpirated
Brought in

## Slide 10
Leaks from
equipments
Wind drift
Runoff or
drainage
Weeds or
excessive storage
Evaporation
Water savings from improvements of... Irrigation efficiency
E=Ed.Ea.Es.Ec.Et=Tpi/Pi
E=[0,1] x ... x [0,1] [0,1]
Examples
E=0.905 = 0.69
E=0.755 = 0.24
Quite drastic effect, nope?
Real-life realistic range
Stage 5

## Slide 11
Leaks from
equipments
Wind drift
Runoff or
drainage
Weeds or
excessive storage
Evaporation
Water savings from improvements of... Irrigation efficiency
E=Ed.Ea.Es.Ec.Et=Tpi/Pi
Efficiency E=Tpi/Pi mm/mm or [-]
Productivity P=Yi/Pi (ton/ha)/mm
Profitability F=Fi(Yi)/Pi (€/ha)/mm
Stage 5
"Then I should definitely increase my irrigation water efficiency"

## Slide 12
Leaks from
equipments
Wind drift
Runoff or
drainage
Weeds or
excessive storage
Evaporation
Water savings from improvements of... Irrigation efficiency
E=Ed.Ea.Es.Ec.Et=Tpi/Pi
Efficiency E=Tpi/Pi mm/mm or [-]
Productivity P=Yi/Pi (ton/ha)/mm
Profitability F=Fi(Yi)/Pi (€/ha)/mm
Stage 5
"Then I should definitely increase my irrigation water efficiency"
"Yes buddy and you should really
start by reducing the losses"

## Slide 13
Leaks from
equipments
Wind drift
Runoff or
drainage
Weeds or
excessive storage
Evaporation
Water savings from improvements of... Irrigation efficiency
"Then I should definitely increase my irrigation water efficiency"
"Yes buddy and you should really
start by reducing the losses"
Technical losses
Various upstream losses
Improper, defective or miscontrolled plot equipment
Tactical losses
Dummy, default or too constrained irrigation strategy

## Slide 14
Leaks from
equipments
Wind drift
Runoff or
drainage
Weeds or
excessive storage
Evaporation
Water savings from improvements of... Irrigation efficiency
"Then I should definitely increase my irrigation water efficiency"
"Yes buddy and you should really
start by reducing the losses"
Tactical improvements vs. Tactical losses
Improving irrigation strategy by tuning irrigation scenarios
v1.7R
Generation, analysis & optimization
of crop irrigation scenarios
Dedicated module that handles irrigation water efficiency

## Slide 15
Water savings from improvements of... Irrigation efficiency
Total soil profile reserve from sowing to harvest (mm)
Efficiency module
Output example 1
Original legend in French
To show the initial conditions
"Ahem these irrigations took place just before rain events"

## Slide 16
Water savings from improvements of... Irrigation efficiency
Cumulative deep drainage from sowing to harvest (mm)
Drainage of irrigation water (mm)
Drainage of rain water (mm)
Irrigation (mm)
Rain (mm)
Efficiency module
Output example 2
"Ok there was drainage of irrigation water here"

## Slide 17
Water savings from improvements of... Irrigation efficiency
Evaporation of irrigation water (mm)
Evaporation of rain water (mm)
Irrigation (mm)
Rain (mm)
Cumulative soil evaporation from sowing to harvest (mm)
Efficiency module
Output example 3
"Some of it is evaporated, some of it expectedly transpirated, huh?"

## Slide 18
Water savings from improvements of... Irrigation efficiency
Efficiency module
Output example 4
Cumulative crop transpiration from sowing to harvest (mm)
Transpiration of irrigation water (mm)
Transpiration of rain water (mm)
Irrigation (mm)
Rain (mm)
"Seems good as more transpiration than evaporation occurs AND the pale blue fraction increases with time "

## Slide 19
Water savings from improvements of... Irrigation efficiency
Summary of the key terms in the efficiency cascade scheme
Upstream losses (mm)
Drainage (mm)
Storage of irrigation water in soil (mm)
Evaporation of irrigation water (mm)
Transpiration of irrigation water (mm)
Global efficiency (-)
Irrigation (mm)
Rain (mm)
Efficiency module
Output example 4
Global efficiency Tpi/Pi
"Ouch my upstream losses hurt and irrigation storage is so damn high!"

## Slide 20
Water savings from improvements of... Irrigation efficiency
"I need to evaluate or reformulate my irrigation strategies, especially in a context of limited resource availability"
" is here for you, and can be tuned to save water by improving irrigation efficiency... but instead of an autograph I made a little drawing for you"

## Slide 21
Water savings from improvements of... Irrigation efficiency
"Think about it:
1- Maximum crop yield is obtained for higher irrigation amounts than these of maximum irrigation efficiency
2- Reducing irrigation to improve efficiency is a virtous behavious that may need/deserve a financial reward"